## Slide 1
The Volume Dividend
Ethanol & biodiesel blending, honest pump prices, state taxation — and the CBG alternative
India · FY 2024-25 volumes · July 2026 prices · SIAM/ARAI FE anchor | repos: india-omc-fuel-fleet-model · vehicle_fuel_mileage

## Slide 2
The physics: a litre is not a litre
Lower heating value per litre (liquids) and per kg (gases)
Chart: 
| Diesel | B20 | Petrol E0 | E10 | E20 | E30 | Isobutanol | Ethanol
MJ per litre | 35.7 | 35.1 | 32.1 | 31 | 29.9 | 28.8 | 26.5 | 21.1
Sold per kilogram
CNG 47.5 MJ/kg
CBG 46.5 MJ/kg
Ethanol carries 34% less energy per litre than petrol; isobutanol only 17% less
Every ethanol blend step dilutes the litre the customer pays for
CBG at IS 16087 spec is at CNG parity per kg — pure methane is above it (50 MJ/kg)

## Slide 3
The mechanism: dilution becomes revenue
Why every per-litre stakeholder quietly gains from blending
Blend 20% ethanol
energy/litre −6.8%
→
Mileage falls
−4% real-world (SIAM/ARAI)
→
Same km, more litres
+4.2% volume through pumps
→
Per-litre levies collect
excise ₹19.90 · VAT ~₹19.5 · dealer ₹4.1 · OMC ₹3.5
₹22,703 cr
extra consumer fuel spend per year at E20 from the volume effect alone —
at an unchanged price per litre. The pump board never shows it.
A 20 km/L hatchback buys +21 L/yr ≈ ₹2,188/yr extra on E20
Hidden levy of 4.2% on every km driven — regressive, invisible
The FY23 ₹2/L penalty on unblended petrol widens the gap further

## Slide 4
Who collects the E20 volume dividend today
₹ crore per year on the 54-billion-litre petrol pool (2.16 bn extra litres)
₹4,303 cr
Centre — excise ₹19.90/L
₹4,216 cr
States — VAT ~₹19.5/L
₹886 cr
Dealers — commission ₹4.1/L
₹757 cr
OMCs — margin ₹3.5/L
Paid entirely by the consumer: ₹22,703 cr/yr
The exchequer + trade gain IS the consumer's loss, litre for litre. This is additive to the separate substitution effect (states forgo VAT on the ethanol fraction).
Dealer commission and OMC margin are volume-linked — network economics quietly improve as blends rise (per-RO throughput has been falling on network dilution; blending offsets it)
OMC-margin figure reconciles exactly with the OMC retail-profitability model (₹757 cr at E20)

## Slide 5
Blending more: E25/E30 and diesel B10–B20
Extra litres pulled through pumps for the same distance (bn L/yr)
Chart: 
| E20 | E25 | E30 | B7 | B10 | B15 | B20
Extra bn L/yr | 2.16 | 3.02 | 3.91 | 0.64 | 0.92 | 1.38 | 1.85
The E20→E30 walk (vs today)
E30 adds +1.75 bn L/yr beyond E20: +₹18,300 cr consumer, +₹6,900 cr excise+VAT, +₹715 cr dealer commission
Engines are calibrated for E20 — the octane-recovery offset is spent; E25–E30 pass through closer to raw energy loss
Diesel pool is 2× petrol: B20 pulls 1.85 bn L despite only −1.7% dilution; cost lands on freight & inflation
Reality check: biodiesel was <1% in FY24-25; NBP targets B5 by 2030

## Slide 6
For the consumer: parity prices that give the mileage back
Honest pricing rule P(blend) = P(E0) × (1 − mileage drop) · petrol at ₹105/L today
E20
₹100.80
−₹4.20/L · 4.0% drop
E25
₹99.22
−₹5.78/L · 5.5% drop
E27
₹98.44
−₹6.56/L · 6.25% drop
proposed sweet spot
E30
₹97.65
−₹7.35/L · 7.0% drop
A parity-priced blend makes cost-per-km identical to unblended petrol — the consumer is made whole, the pump board tells the truth
Restores the consumer's ₹22,700–41,000 cr/yr; the hatchback owner gets the ₹2,188/yr back
E27 mirrors Brazil's ceiling for non-flex engines — the highest blend today's fleet tolerates as E20+ vehicles diffuse

## Slide 7
For the government: parity is already funded
₹/L per blended litre — tax break embedded in the blend vs the discount parity needs
Chart: 
| E20 | E25 | E27 | E30
Embedded tax headroom | 6.46 | 8.07 | 8.72 | 9.69
Parity discount needed | 4.2 | 5.78 | 6.56 | 7.35
Four scenarios tested
S1 pass-through (works, 1.3–1.5×): the ethanol molecule escapes excise + VAT, pays only 5% GST — ₹6.5–9.7/L already sits in the price build-up
S2/S3 duty cuts: possible but costs centre/states ₹22,700–41,000 cr/yr
S4 cheaper ethanol: FAILS — needs ₹37–41/L vs ₹57.97 cheapest feedstock slab; grain mandi prices set the floor (maize slab ₹71.86 is the E30 marginal source)
No new subsidy in S1 — it only stops a windfall the blend walk creates

## Slide 8
Introduce a state SGST on ethanol — price-neutral new revenue
States lose petrol VAT on every ethanol litre; a 1–5% ethanol SGST claws it back inside the fiscal space
Chart: 
| E20 | E22 | E25 | E27 | E30
5% ethanol SGST revenue (₹ cr/yr) | 3243 | 3662 | 4324 | 4787 | 5513
Rate sets the recovery %, blend sets the ₹: 5% recovers ~18% of foregone petrol-VAT at any blend
A 5% levy costs ₹3.0–3.4/L of ethanol — fits inside the ₹7–15/L fiscal space at every blend, so the pump price never moves
Revenue rises on both axes: E20→E30 grows the ethanol base 50%
Sweet spot: E27 @ 5% ≈ ₹4,787 cr/yr of new state revenue at zero consumer cost

## Slide 9
The grand bargain: blend more, charge less, tax smarter
E27 with parity pricing + 5% ethanol SGST — everyone still fits inside the embedded headroom (₹/L of blended petrol)
Embedded headroom at E27
+₹8.72
Consumer parity discount
−₹6.56
States: 5% ethanol SGST
−₹0.89
Slack remaining
+₹1.27
Consumer: ₹98.44/L and honest cost-per-km · States: +₹4,787 cr/yr SGST · Centre: keeps full excise on a bigger blended pool · Farmers: 35% more ethanol offtake
…and let CBG do the gas side
Renewable MJ via SATAT CBG: ₹1.16 vs ethanol's ₹2.94 — 2.5× cheaper
Sold per kg at CNG parity: zero mileage loss, zero hidden levy
CBO at 5% moves the CNG pump just ₹0.59/kg (~0.8%), mileage −0.1%
Undercuts imported LNG above ~$14.8/MMBtu; subsidy sits on-budget (SATAT + GOBARdhan), not in the fuel gauge

## Slide 10
Supply check: higher blends CURE the distillery overcapacity
Capacity utilisation = (fuel + non-fuel ethanol demand) ÷ capacity · CareEdge Ratings May-2026 supply data
Chart: 
| E20 | E25 | E27 | E30
Utilisation on 2,000 cr L (today) | 70 | 85 | 91 | 100
On 2,400 cr L (FY27) | 59 | 71 | 76 | 83
Installed ~2,000 cr L (+400 by FY27); at E20 only ~60% of offered ethanol is absorbed — CareEdge sees 65–75% utilisation for 3 years
E27 lifts utilisation to 76% — top of the band, absorbs Maharashtra's +277 cr L surplus, zero new construction
Coop-mill scheme ≠ capacity: of ₹10,005 cr NCDC gave 56 mills, 96.5% is working capital; the ₹251 cr ethanol tranche ≈ 9.7 cr L/yr (0.5% of installed)
FCI rice leg ~211 cr L (3.9 blend pts, Jul-2023 suspension risk) — the E27/E30 increment rides on open-market maize, the dearest slab
Demand-grown E30 (FY31, 2,173 cr L) hits ~104% — only then does the 4,530 cr L DFPD sanction register need to build

## Slide 11
The RON95 dividend: octane the consumer never sees
RON = knock resistance (regular petrol 91, premium 95) · ethanol blending RON ~112 · BOB = the petrol base before blending
Blend
BOB needed if pump stays RON 91
Pump RON if BOB stays 91
Octane credit ₹/L*
E10
88.7
93.1
4.7
E20
85.7
95.2
9.5
E25
84.0
96.2
11.8
E27
83.2
96.7
12.8
E30
82.0
97.3
14.2
*valued at the retail XP95 spread (~₹2.25/RON point) — a willingness-to-pay ceiling; refining cost is lower (₹0.3–0.8/L per 4–5 points)
net E20 penalty on a RON95-calibrated engine
−1.8%
−4% energy +2.2% from CR 10.5→12
Today India blends to pump RON 91 → refiners quietly drop the blendstock to 85.7 and keep the saving. Holding the blendstock at 91 instead makes E20 a FREE national RON95 fuel — Brazil's E27 playbook: parity pricing compensates today's fleet, RON95 + high-compression E20+ engines erase the penalty as the fleet turns over (~2.9 cr new vehicles/yr)

## Slide 12
What honest blending policy looks like
Price blends for parity: E20 at ₹100.80, stepping to ₹98.44 at E27 — funded by passing through the tax break already embedded (1.3–1.5× coverage; no new subsidy)
Give states a 1–5% SGST on ethanol — up to ₹4,787 cr/yr at E27, price-neutral, ending their structural objection to higher blends
Walk the blend E20 → E27 with the fleet, not ahead of it (Brazil precedent); label pumps with energy content, not just blend %
Label E20+ as RON95 (hold the blendstock at 91) — the free octane lets high-compression engines shrink the mileage penalty to ~−1.8% as the fleet turns over
Keep diesel at B5–B7 until supply and OEM warranties mature — the pool is too big for silent dilution
Scale CBG on the gas side: CNG-parity energy per kg means decarbonisation with no volume dividend to hide — the fiscally honest blend
Full paper: The Volume Dividend (docx/pdf) · github.com/herrrickshaw/india-omc-fuel-fleet-model · vehicle_fuel_mileage