## Slide 1
DME, Done Right
Domestic dimethyl ether for LPG blending — commercial segment first, energy-parity pricing always
Investment pitch · July 2026 · built on the Volume Dividend fourth-quadrant analysis, LERC engineering evidence and BIS IS 18698:2024

## Slide 2
The setup: a huge import bill and a freshly opened standard
…and a trap that will kill naive DME programmes
₹90,000+ cr of LPG imports
India imports ~62% of its 29.7-MMT LPG pool — propane/butane priced off the Saudi CP, dollar-denominated, geopolitically exposed. Every blending programme starts from this bill.
The door is open
BIS IS 18698:2024 permits up to 20% DME in LPG. LERC (LPG Equipment Research Centre, Bengaluru) has cleared 20% material compatibility and run stable flex-burner trials — the engineering is done.
The trap (our own analysis)
DME carries 37% less energy per kg. On subsidised domestic cylinders at unchanged prices, DME20 bills households +₹312/yr AND adds ₹1,201 cr/yr of PMUY subsidy — a programme designed that way dies politically. The pitch is built NOT to be that programme.
LERC's measured thermal-efficiency drop at DME20 is −5.26% (IS 4246) — real but manageable IF the pricing is honest; the venture's entire design flows from that condition

## Slide 3
The guardrails ARE the strategy
Three self-imposed conditions that make the venture durable where naive DME dies
1 · Energy-parity pricing, always
DME sells at LPG price × 28.8/45.8 (~0.63× per kg). The buyer pays for energy, not kilograms. This forgoes the ₹34.7/kg 'temptation margin' — which is precisely the consumer's hidden loss and the programme's political poison.
2 · Commercial LPG first
The 19-kg commercial cylinder is price-DEREGULATED and unsubsidised: parity pricing is a private negotiation, not a subsidy fight. The PMUY inversion never arises. Domestic kitchens only after parity cylinder pricing is regulated in.
3 · Domestic carbon only
Imported-methanol DME earns ₹1.9/kg at honest pricing — it fails, and merely re-denominates the import bill. The venture runs on domestic coal-gasification / bio-methanol under long-term contract, or it does not run.
Honesty as moat: a venture that cannot be accused of the fourth-quadrant harm is the one regulators let scale — the same durability logic as CBG's on-budget stack

## Slide 4
The wedge: commercial & industrial LPG
Unsubsidised, deregulated, price-sensitive buyers — hotels, restaurants, industry
Segment
Pool (MMT/yr)
DME20 ceiling (kt DME)
Why it works
Commercial (19-kg) + industrial
~4.5
~900
deregulated; parity = commercial discount
Auto-LPG
~0.3
~60
niche; elastomer retrofit known
Domestic (14.2-kg, PMUY)
~25
—
EXCLUDED until parity pricing is regulated
The commercial buyer's math
DME20 at energy parity cuts the effective ₹/MJ of a hotel's fuel bill ~2–3% (blender passes part of the DME discount)
Same burners; elastomer swap per LERC compatibility list
Ceiling with today's standard
C&I DME20 ceiling ≈ 0.9–1.1 MMT DME/yr = 27–33 plants of the reference size — years of runway before the domestic segment is even needed

## Slide 5
Business model: the simple step in the chain
100-TPD methanol-to-DME dehydration plant, co-located with domestic methanol capacity
Domestic methanol
coal-gasification / bio-methanol, long-term contract ₹15–17/kg
→
Dehydration unit
catalytic (alumina) — proven, simple; the ₹120 cr asset
→
DME storage & loading
LPG-like handling; pressurised spheres
→
Blender / marketer
OMC & parallel marketers blend ≤20% per IS 18698
→
C&I customer
19-kg cylinders & bulk — energy-parity billed
Per-kg economics at the three postures (₹/kg)
Realisation
Methanol feed (1.4×)
Conversion
Margin
Base: domestic methanol, parity
39.0
(23.8)
(3.5)
11.7
Imported methanol (fails)
39.0
(33.6)
(3.5)
1.9
kg-parity pricing (refused)
62.0
(23.8)
(3.5)
34.7

## Slide 6
Financials: honest pricing still clears 26%
₹120 cr capex · 70:30 @ 10% (no subvention assumed) · 29.7 kt DME/yr · energy-parity realisation ₹39/kg
26.0%
Project IRR
42.1%
Equity IRR
₹106 cr
NPV @ 12%
Year 4
Payback
1.94×
Steady DSCR
Sensitivity — project IRR (%): methanol price × DME realisation
Methanol ₹/kg
₹36/kg
₹39/kg (parity, base)
₹42/kg
15,000/t
25.6
32.4
39.0
17,000/t (base)
18.8
26.0
32.9
20,000/t
6.7
15.6
23.2
The whole model rides on the methanol contract: ₹20/kg methanol compresses IRR to 15.6% — the feed contract IS the investment decision
No subvention assumed — a DME-specific interest-subvention analogue (the ethanol ISS template) is pure upside; EBITDA ₹34.7 cr/yr at base

## Slide 7
Risks and mitigants
Named in our own fourth-quadrant analysis — answered structurally
Risk
Reality
Mitigant
Methanol supply
Domestic coal/bio-methanol capacity is nascent; market methanol is imported ₹24
Co-location + take-or-pay with Coal India/BHEL-route projects; venture gated on the contract, not built ahead of it
Elastomer retrofit
DME attacks conventional seals beyond ~20%
Stay ≤20% per IS 18698; LERC compatibility list is the binding spec; retrofit kits funded at blender
Demand adoption
C&I buyers must accept a blended product
Energy-parity billing makes the buyer strictly better off; pilot with 2 parallel marketers
Policy drift
Pressure to push into subsidised domestic LPG at kg prices
Charter commitment: domestic segment only under regulated parity pricing — the refusal is contractual
Saudi CP swings
Parity realisation moves with LPG
Margin is methanol-linked, not CP-linked, at ~63% pass-through; hedge on the spread
Not relying on: subvention, carbon credits, domestic-kitchen volumes, or any pricing above energy parity

## Slide 8
Landscape: technology proven, field empty
China blends DME-LPG at scale; India has the standard but no supply
Global precedent
China has blended DME into LPG at multi-MMT scale for two decades (the cautionary tales are all kg-parity mis-selling — our guardrail #1 exists because of them). Korea/Japan ran fleet and burner programmes.
Indian building blocks
NCL Pune has demonstrated DME synthesis; IOCL R&D active; Assam Petrochemicals and GNFC hold methanol capacity; Coal India–BHEL coal-to-methanol projects are the feed pipeline. Nobody has assembled the chain.
First-mover reality
India has a 20% standard (IS 18698:2024), LERC-cleared equipment evidence, a ₹90,000-cr import bill — and zero commercial DME blending. The venture IS the market at inception.
Synergy with the bioenergy platform: bio-methanol/bio-DME from CBG-adjacent syngas is the long-run domestic-carbon route — same feedstock ecosystems, same partners

## Slide 9
The ask: one gated pilot, then replicate
₹120 cr
pilot plant (₹36 cr equity)
29.7 kt/yr
DME = ~150 kt DME20 comm. LPG
26% / 42%
project / equity IRR at parity
27–33×
replication ceiling in C&I alone
Gate 1 (pre-capex): 10-yr take-or-pay domestic methanol contract at ≤₹17/kg — no contract, no build; site co-located with the methanol plant
Gate 2: blending MoU with two parallel marketers / one OMC for C&I DME20 at energy-parity transfer pricing; LERC-listed retrofit kits at the bottling plant
Build (15 months) → prove the honest-pricing P&L publicly → replicate toward the ~30-plant C&I ceiling; domestic kitchens only when parity cylinder pricing is regulated
Why fund the constrained version: the unconstrained margin (₹34.7/kg at kg-parity) is exactly what makes naive DME uninvestable — this structure is the one that survives scrutiny, scale and time
Model & sensitivity: dme_pitch_model.py · analysis: dme_lpg_blending.py (LERC basis) · The Volume Dividend §10 · github.com/herrrickshaw/india-omc-fuel-fleet-model